Traffic Light Controller in Verilog

This project implements a traffic light controller for a single road using a finite state machine in Verilog. The controller cycles through Red (5 cycles0, Green (5 cycles). And Yellow (2 cycles) repeatedly. The design was simulated using lcarus Verilog and GTKWave.
Module Code:module traffic_light_controller(
  input clk,
  input reset,
  output reg [2:0] lights );

  reg [2:0] state;
  reg [3:0] counter;
  parameter RED = 3'b100, GREEN = 3'b010 , YELLOW = 3'b001;

  always @(posedge clk or posedge reset )
   begin
      if(reset)
        begin
        state<= RED;
        counter <= 0;
        end
      else
        begin
        counter <= counter + 1;

        case(state)
        RED:
        begin
        if (counter == 4)
        begin
        state <= GREEN;
        counter <= 0;
        end
        end
        GREEN:
        begin
        if(counter == 4)
        begin
        state <= YELLOW;
        counter <= 0;
        end
        end

        YELLOW:
        begin
        if(counter == 1)
        begin
        state <= RED;
        counter <= 0;
        end
        end

        endcase

        end
    end

  always @(*)
    begin
lights = state;
    end

endmodule

        By Rakib Hasnat Akash

Test bench:

module tb_traffic_light;

  reg clk;
  reg reset;
  wire [2:0] lights;

  traffic_light_controller uut(
    .clk(clk),
    .reset(reset),
    .lights(lights)
  );

  initial begin
    clk = 0;
    forever #5 clk = ~clk;
  end

  initial begin
    $dumpfile("traffic_light.vcd");
    $dumpvars(0, tb_traffic_light);

    reset =1;
    #10 reset = 0;

    #200 $finish;
  end

endmodule

Waveform:

The waveform shows the operation of the traffic light controller FSM (Finite State Machine) over time.

clk is the system clock, toggling every 5 time units.

reset is active high and forces the controller into the initial RED state at the beginning.

state changes according to the FSM sequence: RED (3'b100) → GREEN (3'b010) → YELLOW (3'b001) → repeat.

lights[2:0] directly reflects the active state:

State Name	state / Value (Binary)	lights[2:0] / Output	Active Light	Duration (Clock Cycles)
RED	3'b100	100	Red	5
GREEN	3'b010	010	Green	5
YELLOW	3'b001	001	Yellow	2